## Slide 1: Where should Johannesburg grow?
REVIEW OF ANNEXURE 2 | URBAN POTENTIAL MODEL
What the evidence behind our nodes got right, where it falls short, and how we will rebuild it
City Transformation and Spatial Planning | Departmental briefing | October 2026
Notes: Purpose: brief non-technical colleagues on the review of the model behind the 2020 Nodal Review Policy and the decisions taken on its redesign. About 20 minutes plus discussion.

## Slide 2: Why we are looking at this now
2016
SDF 2040 approved. It promised a dedicated review of the city's nodes, based on modelling and public input.
2018
The Urban Potential Model was built and published. It scored every part of the city on access to transport, jobs and services.
2020
Council approved the Nodal Review Policy. Seven zones replaced the old node boundaries.
2026
SPLUMA asks for a five-year refresh. The SDF is under review. The model is now built on data that is 9 to 15 years old.
The question for the Department: is the evidence behind our node boundaries and density rules still good enough to defend, and if not, what do we rebuild?
Notes: Set the context. The nodal review was always meant to be revisited. We are now at that point, and the SDF review makes it timely.

## Slide 3: What the 2018 model did
In plain language, and what the city looks like as a result

## Slide 4: The model in four steps
1. Divide the city into cells
The city was cut into about 10 000 hexagons, each 400 m across. That is a five-minute walk edge to edge.
2. Measure walking access
From the centre of each cell, how many schools, clinics, shops, parks and stations can you walk to in 30 minutes along real streets?
3. Combine into scores
Each count was turned into a 0 to 1 score and blended with fixed weights into two indexes: one for economic nodes, one for residential density.
4. Draw the zones
High scores became nodes, low scores became suburban or peri-urban. Existing nodes and public comments were then used to adjust the lines.
Notes: Keep it simple. The model is essentially a walkability and access scorecard for every 400 m cell in the city.

## Slide 5: What came out of it: seven zones
Chart: 
| Inner City Node | Metropolitan Nodes | Regional Nodes | General Urban Zone | LED Zone | Suburban Zone | Peri-urban Zone | Beyond the UDB
Share of city area | 1.2 | 6.6 | 2.8 | 16.1 | 7.5 | 34.6 | 12.4 | 18.7
10%
of the city's land is in the three node types where the policy wants the most growth
47%
is suburban or peri-urban, where the model sets density by a sliding scale from 5 to 60 units per hectare
Notes: Areas are from the approved 2020 layer. Total 1 704 km². Industrial nodes and the Strategic Area Frameworks sit outside these seven classes.

## Slide 6: What we found
A SWOT and gap analysis of the 2018 method

## Slide 7: The model describes a city that no longer exists
2011
Population
Census 2011 sub-places. Census 2022 is available.
2012
Shops and factories
GeoTerraImage building points, 14 years old.
2013
Taxi routes
Before the 2017 Gauteng taxi mapping.
2016
Streets
OpenStreetMap before most township streets were mapped.
2017
Parks, schools, budget
Pre-dates BRT Phase 1C and the PRASA collapse.
Since then: Census 2022, Waterfall and Modderfontein built out, Rea Vaya Phase 1C, PRASA collapsed and partly recovered, and large-scale backyard densification in Soweto, Diepsloot and Ivory Park.
Every number in the current policy map rests on inputs that are 9 to 15 years old.
Notes: This is the simplest point to land with any audience. The data vintages come straight from Annexure 2.

## Slide 8: What the 2018 model got right
A fair, city-wide yardstick
Every part of the city was measured the same way for the first time, instead of inheriting node lines drawn in 2010.
Built around walking and transit
It measured access along real streets on foot, which is exactly what the SDF's compact-city vision asks for.
Tested with the public
Two rounds of participation, more than 80 written inputs, and every change after comment was written down.
Published and usable
The model, maps and method were put online, and the results were attached to every property in the City's land system.
Notes: Acknowledge the strengths. The redesign builds on these, it does not discard them.

## Slide 9: Where it falls short
It counts shops, not jobs
Economic activity was measured by counting formal commercial buildings. A spaza shop and Sandton City each count as one, and informal trading counts for nothing.
A station is a station
A planned BRT stop, a station with no trains and Gautrain all score the same. Frequency and whether the service runs were never included.
Township economies are invisible
Because only formal buildings were counted, places like Diepsloot scored low. A special LED overlay was added to patch this.
It ignores pipes and power
Whether water, sewer and electricity can carry more growth, and whether land is dolomitic or floods, sit outside the model.
It was never tested against reality
Nobody checked whether the areas it scored highly are where development applications actually came in.
It cannot be re-run
The work lives in old ArcMap, QGIS 2.16 and Excel files. Node lines were partly adjusted by hand with no written rules.
Notes: Six of the twenty weaknesses in the full review. These are the ones that matter for policy credibility.

## Slide 10: Eight gaps that matter most
Measured against what the policy itself promises, what SPLUMA requires, and what other cities now do
1
Job access for the poor
No measure of how long it takes to reach work by taxi, bus or on foot
2
Transit-led density
Stations scored by distance only, with no frequency or operating status
3
Potential vs performance
The index mostly reflects where business already is, not where it could grow
4
Infrastructure feasibility
No link to water, sewer or electricity capacity, which SPLUMA requires us to consider
5
Current data
Inputs are 9 to 15 years old
6
Informal economy
Township trading and backyard growth are not measured
7
Reproducibility
No code and no written rules for hand-drawn boundaries, which weakens us at tribunal
8
Validation
Never tested against seven years of building plans and rezonings
All eight share one root cause: a one-off snapshot built on old, formal-sector data, with no capacity check, no validation and no repeatable rules.
Notes: The full gap analysis has 22 rows. These eight are rated High.

## Slide 11: Opportunities and threats
Opportunities
Census 2022 gives us current population down to small areas
SARS-based employment data (SEAD-SA) tells us where jobs really are
Our own land system, applications and building plans can test the model
Free routing tools can measure travel time by taxi, bus and on foot
Cape Town, London and others have tested designs we can borrow
The SDF review is the right moment to re-base the evidence
Threats
Operators and agencies slow to share transit and jobs data
Legal challenge where a boundary cannot be explained or reproduced
Water, power and rail decline making modelled growth undeliverable
Boundaries bent for single developments, as happened in 2018
Staff turnover losing the files and the know-how again
A redesign so complex that nobody outside the team trusts it
Notes: Opportunities are largely about data that did not exist or was not accessible in 2017. Threats are about delivery and credibility.

## Slide 12: How other cities do it
Cape Town
TOD Comprehensive Model and ECAMP
Models where households and jobs should go to cut transport cost, and scores each business precinct on how it performs today against how well it is located.
London
PTAL and town-centre health checks
Grades every 100 m of the city on walk time to a stop plus how often the service runs. Centres are re-checked on a fixed cycle.
Netherlands
Node-Place model
Scores each station on transport supply and on surrounding land use separately, then asks which is lagging the other.
Portland, USA
State of the Centers report
A recurring report card for every centre: people, jobs, amenities, street connections and transit.
The two ingredients we lack: service frequency on transport, and a clear split between how a place performs now and what it could become.
Notes: None of these cities invented something exotic. They separate transport supply from land-use performance, they use frequency, and they monitor on a cycle.

## Slide 13: The way forward
Decisions taken and what the rebuilt model will do

## Slide 14: Four decisions already taken
Rebuild, do not patch
A full redesign of the index rather than re-running the 2018 method with newer data.
Use the data we can get
SARS-based jobs data, our own land and applications systems, transport schedules, and open data. Licensed building data is not assumed.
Count what is built or budgeted
Operating services and committed projects count. Everything else is shown as a separate scenario so delivery risk is visible.
Serve four aims at once
Job access for low-income households, growth around transit, stronger existing nodes, and growth that infrastructure can carry.
Notes: These were confirmed with the policy owner during the review and are recorded in section 11 of the written report.

## Slide 15: The new approach on one page
Opportunity
How many jobs can you reach in 45 minutes by taxi, bus or on foot?
Transport
How often do services run, and how walkable are the streets around them?
Place
How many jobs, people and mixed uses are already here?
Capacity
Can the pipes, power and land rights carry more growth, and is the land safe to build on?
Densify here
Good transport, little activity
Our nodes
Strong on both
Suburban or peri-urban
Weak on both
Invest in transport first
Busy place, poor transport
Place: weak → strong
Transport and opportunity: weak → strong
Capacity sets how much growth each cell may take, and flags where services must come first.
Zones
Inner City
Metropolitan
Regional
General Urban
LED
Suburban
Peri-urban
Beyond UDB
Classes are set by published thresholds and written rules, not by hand. Every weight is tested to show how much the map moves if it changes.
Notes: Four questions in, a simple sort in the middle, the familiar zones out. The matrix is the Node-Place idea in plain words.

## Slide 16: What will be different this time
 | 2018 model | Rebuilt model
1 | Counted shops within 2 km | Counts jobs and how long it takes to reach them
2 | Any station, any status, same score | Frequency counts; only running or budgeted services count
3 | Services and constraints handled by policy text | Water, power, dolomite and flood lines inside the model
4 | Weights chosen by the modellers | Weights set with departments and tested for sensitivity
5 | Node lines partly adjusted by hand | Published thresholds and a written log of every change
6 | One map, once | A State of the Nodes report on a fixed cycle
7 | Files on one person's computer | A re-runnable model owned by the City
Notes: A before-and-after view is the easiest way for a non-technical audience to grasp the redesign.

## Slide 17: What we need from partners
Transport operators
Rea Vaya, Metrobus, Gautrain and PRASA: schedules in a standard format and a year of passenger numbers. Where no schedule exists, we will build one from timetables.
National Treasury
Access to the SARS-based employment dataset (SEAD-SA) so we can count jobs, not buildings.
Inside the City
Land Use Scheme rights from LIS, seven years of applications and building plans, bulk services capacity from Joburg Water and City Power, and the capital budget with a committed or planned flag.
Province and open sources
School places and clinic headcounts from GDE and Health; Census 2022; the GCRO Quality of Life survey; Gauteng's taxi route mapping.
Notes: Data requests are itemised in section 11.8 of the report with the format wanted for each.

## Slide 18: How the work unfolds
Phase 1
Gather and build
Data requests out, City GTFS built from timetables, pipeline coded on the 2018 logic as a baseline
Phase 2
Test the old model
Check whether the 2018 scores predicted where applications actually came in. Publish the result
Phase 3
Rebuild and consult
Four-pillar model, weights set with departments, draft boundaries out for public comment
Phase 4
Institutionalise
State of the Nodes report, data custodians named, five-year cycle aligned with the SDF
Quick win: Phase 2 can start as soon as the applications and building-plan extracts are in hand. It needs no new data from outside the City.
Notes: Phasing is indicative. Timing depends on data access, which is the main threat.

## Slide 19: An evidence base we can defend
The 2018 model gave the City its first fair yardstick. The rebuilt model will measure jobs, service frequency and capacity, be tested against what was actually built, and be re-run by the City on a fixed cycle.
Asks of this meeting
Endorse the four decisions
Authorise the data requests to operators, Treasury and internal departments
Nominate a model custodian in the Department
Notes: Close on the asks. Full written review is in the Word report circulated with this deck.